This is taken from the www.BasementWatchdog.com website. This is such a great comparison of the Watchdog battery sump pumps. We wanted to share it with you. This cannot be modified in any way. Features BigDog AC/DC Special Emergency POWERFUL Pumping capacity (in gallons per hour at a 10-ft.height) 2200 GPH (3500 GPH@ 0') 1730 GPH (2500 GPH@ 0') 1000 GPH (2000 GPH@ 0') EFFICIENT Efficient 12-volt pump puts less drain on the batteries so they pump longer 10-12 amps 10-12 amps 6.5 amps Approximate hours of continuous pumping with the Basement Watchdog 7.5 hour battery 7.5 hours 7.5 hours 12 hours Approximate hours of continuous pumping with the Emergency sump pump battery Not recommended Not recommended 6 hours Runs intermittently for days on a single charge • • • Charger strength (the higher the amps, the faster it will recharge the battery) 20 amps 1.6 amps .4 amps AUTOMATIC Switches automatically to battery power when AC power fails • • • Pumps automatically when water volume exceeds the capacity of the main AC pump • • • Recharges automatically when power is restored • • • Monitors battery & power conditions constantly • • • Charges the battery, then the charger shuts off to extend the life of the battery • • A battery hooked up backwards will not damage the control unit • • Turns on the pump weekly to ensure operation • Displays the percentage of power remaining in the battery • VERSATILE Pumps on AC power as well as battery power • Capable of pumping and charging the battery simultaneously • Two batteries can be used for double the run time • USER-FRIENDLY Detects irregularities, sounds an alarm, and pinpoints problems and solutions on the control panel • • • The alarm can be silenced during a power outage • • • AN ALARM WILL ALERT YOU TO THESE POTENTIAL PROBLEMS Battery needs water • • • Battery is old and needs to be replaced • • • Battery is discharged • • • Battery is defective and needs to be replaced • • • Battery cable is loose and needs to be tightened • • • Battery terminals need to be cleaned for a better connection • • • Power plug is out of the wall • • • Fuse or circuit breaker has failed • • • Pump has been activated, check the main pump for failure • • • Backup pump is clogged or broken and needs to be cleaned or replaced • Battery is hooked-up improperly • Purchase a basement watchdog battery backup sump pump today!